## Slide 1: TAGE-SC for CBP2025
André Seznec

## Slide 2: TAGE 2006
=?
=?
=?
1
1
1
1
1
1
1
1
1
Hit
Hit
Altpred
Pred
Miss
Use multiple tagged tables
Use “geometric” length
The longest matching table provides the prediction
Except when the prediction counter is weak:
  Selection between Altpred and Pred
Used in many (most ?) designs !!

## Slide 3: TAGE-SC-L predictor (2011, 2014, 2016)
(Main)
TAGE
Predictor
Stat.
Cor.
Prediction + Confidence
Loop Predictor
PPC +Global history
Global, local, IMLI counters
Just a neural predictor

## Slide 4: CBP2016 TAGE-SC-L: not directly implementable
Too many tables in the TAGE component
Too many tables in the SC component
Use of local histories
  A nightmare to manage speculative local histories
And just a huge latency:
  TAGE latency + neural predictor latency
To the best of my knowledge
no official implementation of TAGE-SC-L

## Slide 5
(Main)
TAGE
Predictor
PPC +Global history
Stat.
Cor.
LongestMatchPred HCPRED
IMLI, global history
Mux
LongestMatchPred
HCPRED
4 possible predictions
per branch
1 prediction
per branch
“Realistic” TAGE-SC, Nov 2024
Reasonable number of physical tables
The two components in parallel
  No local history component
TAGE computes two predictions:
  Pred and HCpred
SC speculatively computes 4 predictions
  One for each pair (Pred, HCpred)
Final selection using Pred and HCpred
  HCpred is simpler to compute than Altpred

## Slide 6: Revisiting the alternate prediction
In the initial definition of TAGE:
“Altpred is the prediction if Pred was not hitting”
In practice, Altpred is more difficult than Pred.
This lengthens the prediction time.
Let us use HCPRED the longest hitting “not weak” entry:
If Pred is not weak then HCPRED is identical to Pred
If Pred is weak then HCPRED is distinct

## Slide 8: Let us compete for CBP2025
Take the CBP2016 TAGE-SC code
Insert the innovations from the “realistic” TAGE-SC
  Some tricks on replacement policy for TAGE
  Reengineering (better understanding) of IMLI component
  Use of HCpred instead of Altpred
Use of the dirty tricks of CBP2016:
  Huge number of TAGE tables (and SC)
  Use of local histories

## Slide 9: “Outrageous” optimizations on TAGE
28 histories !!
Global tagged tables sharing
  We end with 28 banks (could have been 30 or 31)
2-way skewed-associative structure on each bank
14 tag bits:
  at the proposed storage budget, the best trade-off is to limit aliasing rather than increase the number of entries

## Slide 10: Geometric series is not that optimal
Seems that:
  Better to concentrate the history lengthes in the middle of the spectrum
  On
  E

## Slide 11: Optimizing allocation/replacement
Replacement is not on the critical path
Base replacement policy uses U counter:
  Monitors if ratio of « useful » entries is below 2/3
  Reaching 2/3 triggers smart U counter reset
Several optimizations from « realistic » TAGE-SC
  Filtering allocation
  First U counter setting
  Protecting recently useful allocated entries
  Updating HCPRED and AltPred on weak Pred mispredicting
TAGE only: 3.781 MPKI, 76 % of the storage budget

## Slide 12: (Let us ignore LOOP PREDICTOR)
Dealing the SC component

## Slide 13: SC tables with PC and TAGE outputs
A single large physical array combining 2 logical tables:
  indexed respectively with hashing of :
    PC + branch number
    PC + branch number +(LongestMatchPred,HCPRED)
        Same index apart 2 bits
A 4-entry table indexed with (LongestMatchPred,HCPRED)
A few small tables using HitBank, Altpred, PC, confidence, ..
TAGE-SC (PC and TAGE): 3.612 MPKI, 78 % of the storage budget

## Slide 14: Global path related SC components
Global path GEHL (8 tables !)
Backward taken history
Forward taken history
256 bytes block history
TAGE-SC (PC, TAGE, global path) 3.522 MPKI, 86% of the storage budget

## Slide 15: What is IMLI ? IMLI= Inner Most Loop Iteration number A. Seznec, J. San Miguel, J. Albericcio “The Inner Most Loop Iteration counter: a new dimension in branch history”, Micro 2015, December 2015
IMLI counter: counts the number of iterations of the last backward branch
Br0
BrI
Efficient to predict branches in the loop body on CBP 2014 traces
Was not that great on CBP 2016 traces
For (j=0; j<N; j++)
For (i=0; i<M;i++)
If (A[i]<0) B[i][j]+=C[i][j]
Strong corelation with the IMLI counter

## Slide 16: Reengineering IMLI: « branch » IMLI
BrIMLI counts the number of consecutive taken backward branches within the same « region »
Monitors the number of iterations in a loop with multiple exits
Monitors the number of iterations in loop nests
Region = 64 bytes
Region N
Region N+1

## Slide 17: Reengineering IMLI: « Target » IMLI
TaIMLI the number of consecutive taken backward branches with their target in the same « region »
Capture the same phenomena as BrIMLI, but adds some coverage

## Slide 18: TAGE-SC including IMLI
4 tables indexed with BrIMLI and TaIMLI for 4 and 64 bytes region
Predict most of the regular loops exits:
  A loop predictor is not worth the effort.
TAGE-SC (PC, TAGE, global path,IMLI) 3.472 MPKI, 89% of the storage budget

## Slide 19: Local history components
4 different local histories
A total of 14 distinct tables
TAGE-SC for CBP2025 3.363 MPKI, 1531 kbits
☠️

## Slide 20: Checkpointed information per branch
13 bits pointer for TAGE history: OK !!
86 bits for global path related SC
  Much less for a realistic design
104 bits for IMLI SC
  Only half if going to a realistic design
5120 bits for local histories:
  I am not aware of any realistic management of speculative local history for 100+ branches deep instruction window
☠️

## Slide 21: Summary
Presented « TAGE-SC for CBP2025 »
  2 % MPKI reduction vs the scaled 192 KB CBP2016 TAGE-SC (from the organizers)
  This is a « limit » study:
    Don’t try to implement in hardware
For a realistic hardware TAGE-SC implementation:
  A. Seznec, TAGE: an engineering cookbook, Inria Nov. 2024
Need for new ideas:
  Other information vectors for SC ?
  Radically new approaches ?
May be in this CBP 😇