## Slide 1: RUNLTS: Register-value-aware predictor Utilizing Nested Large TableS
Toru Koizumi1, Toshiki Maekawa1, Masanari Mizuno1, Maru Kuroki2, Tomoaki Tsumura1, Ryota Shioya2
1Nagoya Institute of Technology, 2The University of Tokyo

## Slide 2: Introduction
The importance of branch prediction is ever increasing.
  A wide frontend (10-way fetch) and a large ROB (1000 entries)
The branch predictor considered to be the most accurate: TAGE-SC(-L)[1]
  TAGE predicts based on the longest match of the global history
  SC refines the TAGE prediction from multiple perspectives, including local histories
Proposed branch predictor: RUNLTS
  Major contribution: Capturing correlations between register values and directions
  Various improvements upon TAGE-SC
  We reduced mispredictions by 6.2% compared with a 192KiB TAGE-SC-L baseline*.
[1] André Seznec. TAGE-SC-L Branch Predictors Again. In Proceedings of the 5th Championship Branch Prediction Workshop (CBP-5), 2016. *: Our tuning.

## Slide 3: RUNLTS structure
High-level structure is almost the same as that of TAGE-SC.
  We added register-value component to the SC.
Statistical corrector predictor (SC)
Table predictor
Bimodal
PC
PC GHR[5:0]
h1
...
h2
alt
h23
...
longest
Table out
[13:0]
Use alt
[4315:0]
Tagged table
Tagged table
Tagged table
...
PC
x1 or xM
UT
Useful
WT0
WT1
WTN
Σ
h0
h1
...
hN
PC, Table out, histories
Final Prediction
SC out
Σ
x
Σ
...
x
Σ
...
...
Register-value component
PC, register values

## Slide 4: RUNLTS features
Register-value component [3.7%]
Table predictor improvements
  Allocation throttling on TAGE [0.5%]
  Novel history length selection [0.2%]
Statistical corrector predictor (SC) improvements
  IMLI weighting [1.2%]
  Call-stack history [0.4%]
  FTL++-like threshold updating method [0.2%]
  Some bias components tuning [0.2%]
[XX%] indicates the MPKI reduction
The sum of these reductions means the improvement of RUNLTS against iso-budget TAGE-SC-L.

## Slide 5: Capturing register-value correlation
Motivation: Register values help in predicting hard-to-predict branches.
Challenges:
  We need to identify correlated registers among the 65 registers.
  The execution results of the last >100 instructions are not yet available at the branch prediction stage because of the pipeline depth and fetch width.
Existing approaches:
  Instruction dependency graph reconstruction + ahead execution or value prediction
Our approach:
  Use a perceptron to find correlated registers.
  Focus on subsequent branch prediction after a branch misprediction has occurred.
    The branch mispredictions will reveal execution results to the branch predictor.
    They are useful for correcting subsequent burst branch misprediction.

## Slide 6: Correlating register values with direction
Conventional SC component:
  Multiple GEHL weight tables, indexed by PC⊕hash(hist[HL[i]:0])
  A usefulness tracking table, indexed by PC
  Weight multiplier
    Useful: 2x / Not useful: 1x
Register value component:
  Multiple weight tables, indexed by PC⊕hash(digest)
    Using 12-bit register-value digest, instead of full 64-bit value
  Per-reg skewed usefulness tracking tables, indexed by hash(PC)
    Useful: 2.5x / Not useful: 0x
    Silencing many non-correlated registers is important.
WT0
PC
WT1
WTN
Σ
x1 or x2
UT
Useful
h0
h1
...
hN
PC + history
WT0
WT1
WT2
Σ
x0 or x2.5
Useful
h0
h1
h2
PC + digest
UT0
UT1
UT2
Σ
PC (skewed)

## Slide 7: Register-value digest
We use 12-bit register-value digest, instead of full 64-bit value.
  It may improve generalization.
For integer registers, XOR the following:
  Trailing ones/zeros
  Leading ones/zeros
  Least significant bits
  → Capture pointer/round number characteristics
For FP registers, use MSBs
  Sign bit and higher part of exponent
  → Capture the magnitude
For flag register, replicate three times
  → Larger Hamming distance
(a) Integer registers
leading one/zero #
trailing one/zero #
Value[5:0]
6
11
(b) FP registers
Value[31:26]
Val[15:13]
Value[63:55]
3
8
FP16
FP32
FP64
(c) Flag register
Value[3:0]
Value[3:0]
Value[3:0]
0
5

## Slide 8: Eliminating multi-ported RAM
Eight-bank structure + using only one of the 9 or 8 registers per bank
Each bank contains:
  8-entry + 8-entry + 8-entry skewed 9-/8-register usefulness tables (UTs)
  512-entry + 256-entry + 128-entry prediction weight tables (WTs)
At prediction: Select the most useful register from the available ones, based on the summed UT values.
At training: Select single register randomly and train for it. (next slide)
  These eliminate multi-ported RAM.
bank 0
512 ent. WT0
256 ent.
WT1
128 ent.
WT2
Σ
x0 or x2.5
h0
h1
h2
PC + reg. digest
9x6bit
8 ent. UT0
8 ent.
UT1
8 ent.
UT2
Σ
9 regs
useful (skewed)
largest
Most useful
in this bank.
bank 1
bank 7
...
Σ
9 regs digest
R0 R8 R16 ... R64
sum
...
PC (skewed)
8 regs digest
...
8 regs digest
...
R1 R9
R7

## Slide 9: Training register value component
For each of the eight banks, train UTs and WTs at every branch resolution (according to the perceptron updating rule[2]).
If any register was used for the prediction, train for the register.
  available and the most useful in the bank
If no register was used for the prediction, randomly select a register that was available at the prediction time, and then train for the register.
  We can use the training port for exploration, eliminating multi-ported RAM.
  Learning becomes slightly slower, but there is no significant accuracy loss.
[2] Daniel A. Jiménez and Calvin Lin. Dynamic branch prediction with perceptrons. In International Symposium on High Performance Computer Architecture (HPCA), pp. 197-206, 2001.

## Slide 10: Tracking available registers
We use Tomasulo-like tabular method.
At decode stage
  Invalidate the digest of destination register
  Record a tag (ROB index)
  (Invalidate too old digests [0.5%])
At execution stage
  Record a digest if the tag matches
At prediction stage
  Use only valid digests
valid
tag or digest
valid
tag or digest
valid
tag or digest
valid
tag or digest
valid
tag or digest
R0
R1
R2
R3
R64

## Slide 11: Allocation throttling on TAGE
Motivation: How aggressively should we allocate tagged entries?
  Too aggressive: causes thrashing 
  Too conservative: slows training on new phases 
The idea of controlled allocation throttling (CAT) is introduced in 2018 by Michaud[3], but the application on TAGE is an open problem.
Our proposal: Storage-free allocation throttling on TAGE
  Throttling based on the ratio of (1) eviction of newly allocated (NA) entry and (2) correct prediction from NA entry... How can this be done without storage?
[3] Pierre Michaud. An Alternative TAGE-like Conditional Branch Predictor. ACM Transactions on Architecture and Code Optimization, Vol. 15, No. 3, Article 30 (2018).

## Slide 12: Storage-free allocation throttling on TAGE
Each TAGE entry contains
  partial tag (~10 bits)
  u-bit (1 bit, tracking usefulness)
  saturating counter (3 bit, for prediction)
We found that specific combinations of {u, ctr} hardly appear.
  → We can safely use these combination for a marker of newly allocated entries.
Count following events and throttle allocation according to their ratio.
  Eviction of marked entry
  Correct prediction provided by marked entry
tag
u
ctr
 |  | ← weak prediction |  | strong prediction → | 
 |  | 0 or -1 | 1 or -2 | 2 or -3 | 3 or -4
not useful | 0 | 4.65% | 2.05% | 3.32% | 76.24%
useful | 1 | 0.02% | 0.99% | 0.98% | 11.75%

## Slide 13: IMLI weighting
IMLI counter: inner most loop iteration counter[4]
  Recently, more robust counting methods were proposed: BrIMLI & TaIMLI[5].
We found that it provides a significant accuracy improvement when a loop contains hard-to-predict (H2P) branches.
→ When IMLI counter component is useful, there are also hard-to-predict branches.
for (i = 0; i < 999; ++i) {
if (!arr[i].valid) {
continue;
}
if (arr[i].data <= th) {
...
}
...
}
Typical example: repeated array traversal with changing only a few entries
IMLI-dir correlation can be captured.
History changes slightly each time; and thus history-dir correlation can hardly be captured.
Our improvements:
Large weight on useful (2x→3x); provide large weight, while
Enlarge per-PC usefulness table; keep small weight for H2Ps.
3x training on useful ; tolerate pollutions from H2Ps.
Large window (64B→128B) ; fit in the large loop.
Predictable
Unpredictable
[4] A. Seznec, J. S. Miguel and J. Albericio, The inner most loop iteration counter: A new dimension in branch history, In Annual IEEE/ACM International Symposium on Microarchitecture (MICRO), pp. 347-357 (2015). [5] TAGE: an engineering cookbook. HAL Inria, RR-9561 (2024). https://hal.science/hal-04804900

## Slide 14: Evaluation: MPKI reduction (S-curve)
Compared to 192KiB TAGE-SC-L*, RUNLTS reduced branch mispredictions for almost all traces.
*: Our tuning.
Higher is better.

## Slide 15: Evaluation: MPKI reduction (S-curve)
Average MPKI reduction: 0.211
First octile MPKI reduction: 0.323
Median MPKI reduction: 0.052
Worst MPKI reduction: -0.024
Best MPKI reduction: 5.727!!

## Slide 16: RUNLTS feature contributions over TAGE-SC-L
Register value component improved wide-range of traces.
Dynamic allocation throttling improved large-footprint traces.
IMLI component largely improved three traces (int.1, int.2, and int.21).
Chart: 
～
～
～
～
～
～
～
～
～
～
compress
fp
infra
int
media
web
Chart: 
| fp.8 | int.1 | int.2 | int.21 | web.7
Others | 0.1299 | 0.0681 | 0.1341 | 0.2693 | 0.0736
Dynamic allocation throttling | 0.0118 | 0.0157 | 0.0425 | 0.0051 | 0.9013
IMLI weighting | 0.013 | 1.2201 | 1.0506 | 0.9438 | 0.0128
Register component | 5.5813 | 0.2581 | 0.2573 | 0.8278 | -0.0299

## Slide 17: Conclusion
Chart: Our Journey to Better Accuracy
| 45780 | 45754.534710648149 | 45754.534710648149 | 45748.173425925932 | 45748.173425925932 | 45742.88244212963 | 45742.88244212963 | 45737.53193287037 | 45737.53193287037 | 45737.365625000006 | 45737.365625000006 | 45737.121412037042 | 45737.121412037042 | 45733.494814814818 | 45733.494814814818 | 45732.45789351852 | 45732.45789351852 | 45727.443182870375 | 45727.443182870375 | 45726.906122685185 | 45726.906122685185 | 45720.181805555556 | 45720.181805555556 | 45719.767800925925 | 45719.767800925925 | 45717.52008101852 | 45717.52008101852 | 45711.356354166666 | 45711.356354166666 | 45710.092569444445
BATAGE(-SC) | 3.159 | 3.159 | 3.163 | 3.163 | 3.166 | 3.166 | 3.173 | 3.173 | 3.176 | 3.176 | 3.181 | 3.181 | 3.213 | 3.213 | 3.214 | 3.214 | 3.222 | 3.222 | 3.275 | 3.275 | 3.3649 | 3.3649 | 3.369 | 3.369 | 3.378 | 3.378 | 3.389 | 3.389 | 3.393 | 3.393
TAGE(-SC-L) | 3.115 | 3.115 | 3.134 | 3.134 | 3.145 | 3.145 | 3.183 | 3.183 | 3.221 | 3.221 | 3.223 | 3.223 | 3.302 | 3.302
RUNLTS | 2.9532 | 2.9545 | 2.9545 | 2.9662 | 2.9662 | 2.9662 | 2.9662 | 2.972 | 2.972 | 2.972 | 2.972 | 2.972 | 2.972 | 2.9738 | 2.9738 | 2.9769 | 2.9769 | 2.9896 | 2.9896 | 3.005 | 3.005 | 3.045 | 3.045 | 3.046 | 3.046 | 3.052 | 3.052 | 3.052 | 3.052 | 3.053 | 3.053 | 3.059 | 3.059 | 3.065 | 3.065 | 3.067 | 3.067 | 3.069 | 3.069 | 3.072 | 3.072 | 3.073 | 3.073 | 3.075 | 3.075 | 3.083 | 3.083 | 3.091 | 3.091 | 3.092 | 3.092 | 3.099 | 3.099 | 3.105 | 3.105 | 3.108 | 3.108 | 3.115
We proposed RUNLTS.
  Major contribution: Capturing correlations between register values and directions
  Various improvements upon TAGE-SC
RUNLTS reduced mispredictions by 6.2% compared to iso-budget TAGE-SC-L.
Note: The vertical axis indicates mispredictions per kilo micro-ops. Sorry!
Register component [3.7%]
Git commit count (right axis)
TAGE-SC-L
BATAGE(-SC)
RUNLTS
Infrastructure development

## Slide 18: Novel history-length selection
We combined second-order arithmetic progression with conventional geometric progression.
Conventional geometric history lengths begin with 4, 5, 7, .... (for example), but the first few intervals are too narrow.
  There should be a very small number of branches where the correlation cannot be captured at history length 4 and can be captured at history length 5.
Starting with second-order arithmetic progression is near-optimal.
History length | 0 |  | 6 |  | 14 |  | 24 |  | 36 |  | 50 |  | 66 |  | 84 |  | 104 |  | 126 |  | 150 |  | 178 |  | 212 |  | 252 |  | 300 |  | 358 |  | 426 |  | 506 |  | 602 |  | 776 |  | 1078 |  | 1606 |  | 2554 |  | 4316 | 
First difference |  | +6 |  | +8 |  | +10 |  | +12 |  | +14 |  | +16 |  | +18 |  | +20 |  | +22 |  | +24 |  | ×1.19 |  | ×1.19 |  | ×1.19 |  | ×1.19 |  | ×1.19 |  | ×1.19 |  | ×1.19 |  | ×1.19 |  | ×1.29 |  | ×1.39 |  | ×1.49 |  | ×1.59 |  | ×1.69 |  | 
Second difference |  |  | 2 |  | 2 |  | 2 |  | 2 |  | 2 |  | 2 |  | 2 |  | 2 |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.1 |  | 0.1 |  | 0.1 |  | 0.1 |  | 0.1 |  |  | 

## Slide 24
128K-entry
Bimodal
20 KiB
PC
Crossbar
u
ctr
tag
... 9 banks
Crossbar
25 banks
...
...
...
PC GHR[5:0]
h1
...
...
h2
h3
h4
...
alt
h5
h23
...
longest
Low banks
4 components
High banks
19 components
Table out
[13:0]
Use alt
Crossbar
Crossbar
[23:0]
[35:0]
[49:0]
[4315:0]
2K entries

## Slide 25
bank 0
Bias
PC
BiasSK
BiasBank
Table Out
Conf
HitBank
AltTaken
Σ
x1 or x2
8 ent.
UT
Useful
sB
WT0
PC
WT1
WTN
Σ
x1 or xM
L ent.
UT
Useful
h0
h1
...
hN
PC + histories
sG: global back + Table Out:
sP: forward taken path:
sC: call stack:
sI: Br+Ta IMLI:
sL: 256ent. local:
sS: 16ent. local:
sT: 16ent. local:
512 ent. WT0
256 ent.
WT1
128 ent.
WT2
Σ
x0 or x2.5
h0
h1
h2
PC + reg. digest
9x6bit
8 ent. UT0
8 ent.
UT1
8 ent.
UT2
Σ
9 regs
useful (skewed)
largest
Most useful
in this bank.
bank 1
bank 7
...
Σ
9 regs digest
R0 R8 R16 ... R64
sG,sP,sC,sI,sL,sS,sT
sR
...
Σ
LSUM
sB,sG,sP,sC,sI,sL,sS,sT,sR
...
L=8,M=2,N=3
L=8,M=2,N=3
L=8,M=2,N=5
L=256,M=3,N=2(Br/Ta)
L=8,M=2,N=4
L=8,M=2,N=4
L=8,M=2,N=4
 | Table High Conf | Table Mid Conf | Other
¦LSUM¦>Th/2 | SC (LSUM>=0) | SC | SC
¦LSUM¦>Th/4 | Meta1 | SC | SC
Other | Table Out | Meta2 | SC
PC
(a) Bias Components
(b) History Components
(c) Proposed Register Components
(d) Decision
8 regs digest
...
8 regs digest
...